This document describes the Gem6K Ethernet implementation for those developing their own Ethernet drivers.  If you are using the communications server (com6srvr.exe) that is included with Motion Planner then you do not need to refer to this document.

This specification pertains to:

- Gem6K operating system revision 5.1.2 and greater

# Gem6K Ethernet Description

The Gem6K series of drive/controllers contains an Ethernet interface for communication. Four ports are available for connection:

- The alarm/variable port (port 5001) is used to set Gem6K variables and receive Gem6K status information in a binary format.

- The communication port (port 5002) is used to transmit and receive the standard Gem6K ASCII command set.

- The status port (port 5003) is used to enable and set a status update interval and retrieve that status information in a binary format.

- The watchdog port (port 5004) is used to monitor the integrity of the Ethernet connection.

The Gem6K acts as a server and executes a passive open on the TCP/IP ports (5001, 5002 and 5004).  The UDP/IP port (5003) is available when the communication port (5002) connects.

The Gem6K utilizes a 68340 microprocessor which requires that the multi-byte fields be transmitted and received with the most significant byte first and the least significant byte last.

For information on the Gem6K Ethernet commands, see the Gem6K Series Command Reference and the Gem6K User Guide Addendum.

# PORT 5001  (TCP/IP Variables & Single Shot Status)

## A. Receive Description

This port receives 192 bytes per packet to set Gem6K variables or to request a status update transmitted on this port. The data is memory mapped, thus, 192 bytes must be sent per packet.

The first 4 bytes comprise the variable mask to identify which variables are being modified in this transmission. The next 8 bytes are reserved for future use (set the bytes to 0).  The next 4 bytes comprise another mask of which bits 0 and 1 are the only ones used at present. If bit 0 is set, then the status information is transmitted on this port. If bit 1 is set, then the status information expands to include real variables.  The other bits are reserved and should be set to 0.

- Integer variables (VARI) are signed 32 bit numbers.

- Variables (VAR) are signed 64 bit numbers in units of 100 millionths.

- Binary variables (VARB) are 32 bit numbers.

### Receive Packet (port 5001) Data Description:

| Function | Size | Description (*) Indicates bit information included below |
| --- | --- | --- |
| Variable Mask | 4 bytes | Variable mask to identify variables modified in this transmission. (see bit descriptions below) |
| Reserved | 4 bytes | Reserved (set to 0) |
| Reserved | 4 bytes | Reserved (set to 0) |
| Action Mask | 4 bytes | Triggers fast status update request |
| Integer Variable 1 | 4 bytes | Contents of VARI1 |
| Integer Variable 2 | 4 bytes | Contents of VARI2 |
| Integer Variable 3 | 4 bytes | Contents of VARI3 |
| Integer Variable 4 | 4 bytes | Contents of VARI4 |
| Integer Variable 5 | 4 bytes | Contents of VARI5 |
| Integer Variable 6 | 4 bytes | Contents of VARI6 |
| Integer Variable 7 | 4 bytes | Contents of VARI7 |
| Integer Variable 8 | 4 bytes | Contents of VARI8 |
| Integer Variable 9 | 4 bytes | Contents of VARI9 |
| Integer Variable 10 | 4 bytes | Contents of VARI10 |
| Integer Variable 11 | 4 bytes | Contents of VARI11 |
| Integer Variable 12 | 4 bytes | Contents of VARI12 |
| Real Variable 1 | 8 bytes | Contents of VAR1 |
| Real Variable 2 | 8 bytes | Contents of VAR2 |
| Real Variable 3 | 8 bytes | Contents of VAR3 |

| Real Variable 4 | 8 bytes | Contents of VAR4 |
| --- | --- | --- |
| Real Variable 5 | 8 bytes | Contents of VAR5 |
| Real Variable 6 | 8 bytes | Contents of VAR6 |
| Real Variable 7 | 8 bytes | Contents of VAR7 |
| Real Variable 8 | 8 bytes | Contents of VAR8 |
| Real Variable 9 | 8 bytes | Contents of VAR9 |
| Real Variable 10 | 8 bytes | Contents of VAR10 |
| Real Variable 11 | 8 bytes | Contents of VAR11 |
| Real Variable 12 | 8 bytes | Contents of VAR12 |
| Binary Variable 1 | 4 bytes | Contents of VARB1 |
| Binary Variable 2 | 4 bytes | Contents of VARB2 |
| Binary Variable 3 | 4 bytes | Contents of VARB3 |
| Binary Variable 4 | 4 bytes | Contents of VARB4 |
| Binary Variable 5 | 4 bytes | Contents of VARB5 |
| Binary Variable 6 | 4 bytes | Contents of VARB6 |
| Binary Variable 7 | 4 bytes | Contents of VARB7 |
| Binary Variable 8 | 4 bytes | Contents of VARB8 |

Variable Mask Bit Information

| Bit | Setting | Action |
| --- | --- | --- |
| 0 | 1 | Enables setting VARI1 |
| 1 | 1 | Enables setting VARI2 |
| 2 | 1 | Enables setting VARI3 |
| 3 | 1 | Enables setting VARI4 |
| 4 | 1 | Enables setting VARI5 |
| 5 | 1 | Enables setting VARI6 |
| 6 | 1 | Enables setting VARI7 |
| 7 | 1 | Enables setting VARI8 |
| 8 | 1 | Enables setting VARI9 |
| 9 | 1 | Enables setting VARI10 |
| 10 | 1 | Enables setting VARI11 |
| 11 | 1 | Enables setting VARI12 |
| 12 | 1 | Enables setting VAR1 |
| 13 | 1 | Enables setting VAR2 |
| 14 | 1 | Enables setting VAR3 |
| 15 | 1 | Enables setting VAR4 |
| 16 | 1 | Enables setting VAR5 |
| 17 | 1 | Enables setting VAR6 |
| 18 | 1 | Enables setting VAR7 |
| 19 | 1 | Enables setting VAR8 |
| 20 | 1 | Enables setting VAR9 |
| 21 | 1 | Enables setting VAR10 |
| 22 | 1 | Enables setting VAR11 |
| 23 | 1 | Enables setting VAR12 |
| 24 | 1 | Enables setting VARB1 |
| 25 | 1 | Enables setting VARB2 |
| 26 | 1 | Enables setting VARB3 |
| 27 | 1 | Enables setting VARB4 |
| 28 | 1 | Enables setting VARB5 |
| 29 | 1 | Enables setting VARB6 |
| 30 | 1 | Enables setting VARB7 |
| 31 | 1 | Enables setting VARB8 |

## B. Transmit Description

The port transmits 288 bytes per packet that contains data.  The data is memory mapped, thus, 288 bytes are always sent per transmission.  Data is transmitted when bit 0 of the action mask is set, when the NTSFS command is executed in the Gem6K or when an enabled alarm event occurs.  Alarm events are enabled with the Gem6K command INTHW.

The commanded position and encoder positions are signed 32 bit numbers.  The commanded velocity is an unsigned 32 bit number.  The Status values are 32 bit numbers where each bit represents a state or mode setting.  See the Gem6K Command Reference Guide for the bit assignments.  The time frame counter is a running counter in 2.022 millisecond increments (if SYSPER4 is set, then the counter is in 4.044 millisecond increments).  The command counter indicates the number of commands executed since

power-up or reset outside of a program. The analog input values are in ADC counts represented as signed 16 bit words.

### Transmit Packet (port 5001) Data Description:

| Function | Size | Description |
| --- | --- | --- |
| Update Mode | 2 bytes | If non-zero, Gem6K will transmit fast status information at an interval specified in Port 5003. |
| Time Frame Counter | 2 bytes | Free running counter in 2.022 or 4.044 ms |
| Commanded Position | 4 bytes | See TPC command |
| Encoder Position | 4 bytes | See TPE command |
| Commanded Velocity | 4 bytes | See TVEL command |
| Axis Status | 4 bytes | See TAS command |
| System Status | 4 bytes | See TSS command |
| Error Status | 4 bytes | See TER command |
| User Status | 4 bytes | See TUS command |
| Timer Value | 4 bytes | See TTIM command |
| Limit Status | 4 bytes | See TLIM command |
| Onboard Input Status | 4 bytes | See TIN command |
| Brick 1 Input Status | 4 bytes | See TIN command |
| Brick 2 Input Status | 4 bytes | See TIN command |
| Brick 3 Input Status | 4 bytes | See TIN command |
| Onboard Output Status | 4 bytes | See TOUT command |
| Brick 1 Output Status | 4 bytes | See TOUT command |
| Brick 2 Output Status | 4 bytes | See TOUT command |
| Brick 3 Output Status | 4 bytes | See TOUT command |
| Trigger Status | 4 bytes | See TTRIG command |
| Analog Input Value | 4 bytes | See TANI command |
| Binary Variable 1 | 4 bytes | VARB1 |
| Binary Variable 2 | 4 bytes | VARB2 |

| Binary Variable 3 | 4 bytes | VARB3 |
| --- | --- | --- |
| Binary Variable 4 | 4 bytes | VARB4 |
| Binary Variable 5 | 4 bytes | VARB5 |
| Binary Variable 6 | 4 bytes | VARB6 |
| Binary Variable 7 | 4 bytes | VARB7 |
| Binary Variable 8 | 4 bytes | VARB8 |
| Binary Variable 9 | 4 bytes | VARB9 |
| Binary Variable 10 | 4 bytes | VARB10 |
| Integer Variable 1 | 4 bytes | VARI1 |
| Integer Variable 2 | 4 bytes | VARI2 |
| Integer Variable 3 | 4 bytes | VARI3 |
| Integer Variable 4 | 4 bytes | VARI4 |
| Integer Variable 5 | 4 bytes | VARI5 |
| Integer Variable 6 | 4 bytes | VARI6 |
| Integer Variable 7 | 4 bytes | VARI7 |
| Integer Variable 8 | 4 bytes | VARI8 |
| Integer Variable 9 | 4 bytes | VARI9 |
| Integer Variable 10 | 4 bytes | VARI10 |
| IP Address | 4 bytes | Gem6K IP Address |
| Command Counter | 4 bytes | Total number of commands executed since power up. |
| *Real Variable 1 | 8 bytes | VAR1 |
| *Real Variable 2 | 8 bytes | VAR2 |
| *Real Variable 3 | 8 bytes | VAR3 |
| *Real Variable 4 | 8 bytes | VAR4 |
| *Real Variable 5 | 8 bytes | VAR5 |
| *Real Variable 6 | 8 bytes | VAR6 |
| *Real Variable 7 | 8 bytes | VAR7 |
| *Real Variable 8 | 8 bytes | VAR8 |
| *Real Variable 9 | 8 bytes | VAR9 |
| *Real Variable 10 | 8 bytes | VAR10 |
| *Real Variable 11 | 8 bytes | VAR11 |
| *Real Variable 12 | 8 bytes | VAR12 |
| Actual Acceleration | 4 bytes | See TACCA command |
| Extended Axis Status | 4 bytes | See TASX command |
| Configuration Status | 2 bytes | See TCS command |
| Settling Time | 2 bytes | See TSTLT command |
| Commanded Torque | 2 bytes | See TTRQ command |
| Actual Torque | 2 bytes | See TTRQA command |
| Actual Velocity | 4 bytes | See TVELA command |
| Alarm Status | 4 bytes | Bit status of alarm conditions (see bit descriptions below) |

Alarm Status Information

| Bit | Setting | Action |
| --- | --- | --- |
| 0 | 1 | User Software Alarm 1 |
| 1 | 1 | User Software Alarm 2 |
| 2 | 1 | User Software Alarm 3 |
| 3 | 1 | User Software Alarm 4 |
| 4 | 1 | User Software Alarm 5 |
| 5 | 1 | User Software Alarm 6 |
| 6 | 1 | User Software Alarm 7 |
| 7 | 1 | User Software Alarm 8 |
| 8 | 1 | User Software Alarm 9 |
| 9 | 1 | User Software Alarm 10 |
| 10 | 1 | User Software Alarm 11 |
| 11 | 1 | User Software Alarm 12 |
| 12 | 1 | Command Buffer Full |
| 13 | 1 | Enable Input Not Grounded |
| 14 | 1 | Program Complete |
| 15 | 1 | Drive Fault |
| 16 | 1 | Reserved |
| 17 | 1 | Reserved |
| 18 | 1 | Limit Hit |
| 19 | 1 | Stall Detected |
| 20 | 1 | Timer |
| 21 | 1 | Ethernet Failure |
| 22 | 1 | Alarm Input |
| 23 | 1 | Command Error |
| 24 | 1 | Motion Complete |
| 25 | 1 | Reserved |
| 26 | 1 | Reserved |
| 27 | 1 | Reserved |
| 28 | 1 | Reserved |
| 29 | 1 | Reserved |
| 30 | 1 | Reserved |
| 31 | 1 | Reserved |

# PORT 5002  (TCP/IP ASCII Commands)

## A. Receive Description

This port receives standard Gem6K ASCII commands.  Connecting to this port disables RS232 port 1. This connection acts as the Gem6K's communication port 1.

## B. Transmit Description

This port transmits ASCII in response to a Gem6K command.  The Gem6K communication settings (EOL, EOT, ERRLVL, etc) that frame the response are those of port 1.

# PORT 5003  (UDP/IP Fast Status Update)

## A. Receive Description

This port receives 4 bytes per packet to configure the status update interval.  The data is memory mapped, thus, 4 bytes must be sent per transmission.  The first two bytes set the update mode, if nonzero

then the next two bytes set the rate in milliseconds that the status data will be automatically transmitted.

### Receive Packet (port 5003) Data Description:

| Function | Size | Description |
| --- | --- | --- |
| Update mode | 2 bytes | Sets the mode to update fast status information if non-zero. |
| Update interval | 2 bytes | Sets the fast status update interval in milliseconds. |

## B. Transmit Description

The port transmits 284 bytes per packet which contains data   The data is memory mapped, thus, 284 bytes are always sent per transmission.

The commanded position and encoder positions are signed 32 bit numbers.  The commanded velocity is an unsigned 32 bit number.  The Status values are 32 bit numbers where each bit represents a state or mode setting.  See the Gem6K Command Reference Guide for the bit assignments.  The time frame counter is a running counter in 2.022 millisecond increments (if SYSPER4 is set, then the counter is in 4.044 millisecond increments).  The command counter indicates the number of commands executed since

power-up or reset outside of a program. The analog input values are in ADC counts represented as signed 16 bit words.

### Transmit Packet (port 5003) Data Description:

| Function | Size | Description |
| --- | --- | --- |
| Update Mode | 2 bytes | If non-zero, Gem6K will transmit fast status information at an interval specified in Port 5003. |
| Time Frame Counter | 2 bytes | Free running counter in 2.022 or 4.044 ms |
| Commanded Position | 4 bytes | See TPC command |
| Encoder Position | 4 bytes | See TPE command |
| Commanded Velocity | 4 bytes | See TVEL command |
| Axis Status | 4 bytes | See TAS command |
| System Status | 4 bytes | See TSS command |
| Error Status | 4 bytes | See TER command |

| User Status | 4 bytes | See TUS command |
| --- | --- | --- |
| Timer Value | 4 bytes | See TTIM command |
| Limit Status | 4 bytes | See TLIM command |
| Onboard Input Status | 4 bytes | See TIN command |
| Brick 1 Input Status | 4 bytes | See TIN command |
| Brick 2 Input Status | 4 bytes | See TIN command |
| Brick 3 Input Status | 4 bytes | See TIN command |
| Onboard Output Status | 4 bytes | See TOUT command |
| Brick 1 Output Status | 4 bytes | See TOUT command |
| Brick 2 Output Status | 4 bytes | See TOUT command |
| Brick 3 Output Status | 4 bytes | See TOUT command |
| Trigger Status | 4 bytes | See TTRIG command |
| Analog Input Value | 4 bytes | See TANI command |
| Binary Variable 1 | 4 bytes | VARB1 |
| Binary Variable 2 | 4 bytes | VARB2 |
| Binary Variable 3 | 4 bytes | VARB3 |
| Binary Variable 4 | 4 bytes | VARB4 |
| Binary Variable 5 | 4 bytes | VARB5 |
| Binary Variable 6 | 4 bytes | VARB6 |
| Binary Variable 7 | 4 bytes | VARB7 |
| Binary Variable 8 | 4 bytes | VARB8 |
| Binary Variable 9 | 4 bytes | VARB9 |
| Binary Variable 10 | 4 bytes | VARB10 |
| Integer Variable 1 | 4 bytes | VARI1 |
| Integer Variable 2 | 4 bytes | VARI2 |
| Integer Variable 3 | 4 bytes | VARI3 |
| Integer Variable 4 | 4 bytes | VARI4 |
| Integer Variable 5 | 4 bytes | VARI5 |
| Integer Variable 6 | 4 bytes | VARI6 |
| Integer Variable 7 | 4 bytes | VARI7 |
| Integer Variable 8 | 4 bytes | VARI8 |
| Integer Variable 9 | 4 bytes | VARI9 |
| Integer Variable 10 | 4 bytes | VARI10 |
| IP Address | 4 bytes | Gem6K IP Address |
| Command Counter | 4 bytes | Total number of commands executed since power up. |
| *Real Variable 1 | 8 bytes | VAR1 |
| *Real Variable 2 | 8 bytes | VAR2 |
| *Real Variable 3 | 8 bytes | VAR3 |
| *Real Variable 4 | 8 bytes | VAR4 |
| *Real Variable 5 | 8 bytes | VAR5 |
| *Real Variable 6 | 8 bytes | VAR6 |
| *Real Variable 7 | 8 bytes | VAR7 |
| *Real Variable 8 | 8 bytes | VAR8 |
| *Real Variable 9 | 8 bytes | VAR9 |
| *Real Variable 10 | 8 bytes | VAR10 |
| *Real Variable 11 | 8 bytes | VAR11 |
| *Real Variable 12 | 8 bytes | VAR12 |
| Actual Acceleration | 4 bytes | See TACCA command |
| Extended Axis Status | 4 bytes | See TASX command |
| Configuration Status | 2 bytes | See TCS command |
| Settling Time | 2 bytes | See TSTLT command |
| Commanded Torque | 2 bytes | See TTRQ command |
| Actual Torque | 2 bytes | See TTRQA command |
| Actual Velocity | 4 bytes | See TVELA command |

# PORT 5004  (TCP/IP Watchdog)

## A. Receive Description

This port receives 12 bytes per packet to configure the watchdog timer.  The first two bytes configures the time interval in seconds and the second two bytes configures the number of retries a packet is to be

transmitted during the time interval.

### Receive Packet (port 5004) Data Description:

| Function | Size | Description |
| --- | --- | --- |
| Watchdog Timer | 2 bytes | Time interval in seconds for watchdog. |
| Watchdog Ticker | 2 bytes | Number of retries per time interval before watchdog times out. |
| Reserved | 8 bytes | Reserved for future use and should be set to zero. |

## B. Transmit Description

The port immediately echoes the Receive Packet Data for Port 5004.

### Transmit Packet (port 5004) Data Description:

| Function | Size | Description |
| --- | --- | --- |
| Watchdog Timer | 2 bytes | Time interval in seconds for watchdog. |
| Watchdog Ticker | 2 bytes | Number of retries per time interval before watchdog times out. |
| Reserved | 8 bytes | Reserved. These will be all zero. |